## Slide 1: Framework ICT – PreAward-eCat- Pre_Award_eCatalogue_Architectural_Framework 1.01
Editors: Giancarlo De Stefano, Consip
Leonardo Bertini, Consip
Selmin Ustaoglu, Consip
Version: 1.0.1
Status: In use

## Slide 2: Statements
Statement of originality
This deliverable contains original unpublished work except where clearly indicated otherwise. Acknowledgement of previously published material and of the work of others has been made through appropriate citation, quotation or both.
Statement of copyright
This deliverable is released under the terms of the Creative Commons Licence accessed through the following link: http://creativecommons.org/licenses/by/3.0/.
In short, it is free to
Share — to copy, distribute and transmit the work Remix — to adapt the work
Under the following conditions
Attribution — You must attribute the work in the manner specified by the author or licensor (but not in any way that suggests that they endorse you or your use of the work).

## Slide 3: Revision History
Version | Date | Editor | Org | Description
1.00 | 01.06.2011 | Giancarlo De Stefano | Consip | First Release
1.0.1 | 30.06.2012 | Giancarlo De Stefano | Consip | Update for alignement with PEPPOL EIA Release 4 and Transfer of Ownership

## Slide 4: General Architecture of PEPPOL Solutions
Application
Application
Interface
Application
Transformation
START
Interface
Other
Interface
Application
Interface
Transform.
Valid.
Infrastructure Access point of the Receiver
START
Interface
Other
Interface
PEPPOL Building Blocks scope
Validation
Infrastructure Access point of the Sender
Sender
Receiver

## Slide 5: The PEPPOL Pre-Award eCatalogue High Level Framework
(eCatalogue Components)
a | s | ss | a | s
Page 5
Catalogue Content Server
Web service
eCatalogue Template publication
Download
eCatalogue offer submission (manual or via eDelivery)
Contracting Authority
Mapping of existing Catalogues to the Template info (including integration linking to existing Dictionaries)
(eCatalogue Components; Demo tool)
a | s | ss | a | s
1 | 4 | 7 | 8 | 3
6 | T | as | P | G
<catalogue_header>
<supplier_party.supplier>
<name>
CompanyX
<name>
<supplier_address>
<street_name>
Via dell’olmo
<street_name>
<street_number>
12
<street_number>
Economic operator
(PPS specific’s, Standard dictionary)

## Slide 6
Page 6
How does the PEPPOL general framework look like for pre-award eCatalogues?

## Slide 7: The PEPPOL eCatalogue ICT Architecture Framework
(eCatalogue Components)
a | s | ss | a | s
Page 7
On line Product Property Server
(1) The CA calls a web service from an on-line Dictionary to retrieve standardized product properties….
(3) The CA publishes the eCat Template on its tendering site
(4) Ec. Operators download the eCat Template….
…(7) and finally upload it (or send) to the CA platform
Contracting Authority
(5) Ec. Operators import and fill-in the template
(eCatalogue Components; Demo tool)
a | s | ss | a | s
1 | 4 | 7 | 8 | 3
6 | T | as | P | G
a | s | ss | a | s
… and (2) creates a Catalogue Template (i.e. a document with specified structure, and content: classification+properties)
… then (6) create XML eCatalogue file, validate it (sign), ….
<catalogue_header>
<supplier_party.supplier>
<name>
CompanyX
<name>
<supplier_address>
<street_name>
Via dell’olmo
<street_name>
<street_number>
12
<street_number>
Economic operator
(PPS specific’s, Standard dictionary)

## Slide 8: ICT Architecture Description 1/8
  Step1 : The CA calls a web service from an on-line Dictionary to retrieve standardized product properties: The Contracting Authority eProcurement platform (with PEPPOL eCatalogue PRAS component) calls a web service from a (PEPPOL) Property Server (PPS) (=on-line Dictionary of standardized properties) to retrieve standardized product properties based on a standardized dictionary, and supports/leads the Contracting Authority Officer in identifying the properties that best suit his/her view of how the items to purchase should be described. The original description (=set of properties) of the item included in the classification system can be extended, adding properties coming from other products, and creating a new property, where needed.
  * Note: in the following, the functions described for the Contracting Authority eProcurement platform could be performed by the PEPPOL Pre-award Demo tools.

## Slide 9: ICT Architecture Description 2/8
  In the case of “bundled products” (products composed of a bundling of items) the starting point for the configuration is the description (=set of properties) of the item as included in the classification system. The description of an item generates an ‘item template’, that can be posted in the PPS for use by other Contracting Authorities. In addition, the server supports the Contracting Authority Officer in the creation of the “business rules” that are associated to the item template, such as: minimum/maximum values; compulsory/optional attributes; relationships between attributes; etc. When an item is described appropriately, the item templates can be ‘pasted’ in the eCatalogue Template hosted in the Contracting Authority eProcurement platform.

## Slide 10: ICT Architecture Description 3/8
  Step 2 : The Contracting Authority eProcurement platform supports CA to create a Catalogue Template (i.e. a document with specified structure and std properties) When all the standardized item templates are acquired, the platform is ready to generate the “eCatalogue template” (i.e. the combination of standard format and standard description of the items to be purchased) that the Economic Operators will have to use to submit their offers. The platform will generate the XML document that represents the template, based on the data model included in the PEPPOL BIS 12a.

## Slide 11: ICT Architecture Description 4/8
  Step 3: The CA publishes the eCat Template on its tendering site The Contracting Authority publishes on-line the eCatalogue template and the associated business rules, together with other tender documentation on its tendering site (no support from PEPPOL tools in this step).

## Slide 12: ICT Architecture Description 5/8
  Step 4: Economic Operators download the eCat Template The interested Economic Operators download the eCatalogue template and the associated business rules, together with other tender documentation (no support from PEPPOL tools in this step).

## Slide 13: ICT Architecture Description 6/8
  Step 5: Econimic Operator imports the template on its platform, and fills it in with integrated PEPPOL Components (which supports linking to the PPS if needed) The Economic Operators imports the eCatalogue template on its platfomr as an XML format, and fills-in the template by using PEPPOL pre-award eCat Components integrated into its own platform

## Slide 14: ICT Architecture Description 7/8
  Step 6: Ec Op can create and validate their eCatalogue Offer The Economic Operator creates the eCatalogue Offer in a PEPPOL-compliant XML format, which includes item properties based on the same standard classification system and standard attributes used in the eCatalogue template created by the Contracting Authority. In the pre-award phase the eCatalogue offer is data model is based on the one included in the PEPPOL BIS 12a.

## Slide 15: ICT Architecture Description 8/8
  Step 7: eCatalogue Offer is finally uploaded (or sent) to the CA platform Upon generation of the PEPPOL-compliant pre-award XML eCatalogue document, the Economic Operator signs it together with the other offer documents for the specific tender (if the submission of the signed offer is prescribed by national legislation; In this case, the Economic Operator will resort to its own tools for the signature of the eCatalogue). The Economic Operator will upload the document in the Contracting Authority eTendering platform according to the tender instructions.

## Slide 16
Page 16
Architecture components

## Slide 17: PEPPOL Property Service- PPS
  Central (need to have)
  Service description : Peppol Property Service is a Web Service that provides:
    multilingual classification codes (CPV + others)
    standardized description of product attributes
    creation and posting of “item templates”

## Slide 18: Contract Authority (CA) Tool
  Decentral (optional to have)
  Service description : The tool is an integrated collection of transformation, validation, visualization and web service components, which can be integrated in national platforms, allowing the creation of PEPPOL-compliant (=according to PEPPOL data model) pre-award eCatalogue templates, with fully standardized content (catalogue format and product descriptions) DEMO http://www.phloc.com/peppol/view/p-1005/Demo-Client-Download/

## Slide 19: Economic Operator (EcOp) Tool
  Decentral (optional to have)
  Service description : The Tool is an integrated collection of transformation, validation, visualization and web service components, which can be integrated in national platforms, allowing the creation of PEPPOL-compliant (=according to PEPPOL data model) pre-award eCatalogue tenders, with fully standardized content DEMO http://www.phloc.com/peppol/view/p-1005/Demo-Client-Download/

## Slide 20: Validation Component
Page 20
  Decentral
  A stand alone runtime Java application in Open Source, that can be installed in any Java platform to perform validation of PreAward eCatalogues against the PEPPOL BIS Business Rules

## Slide 21: Transformation Component - ODS
Page 21
  Decentral
  A stand alone runtime Java application in Open Source, that can be installed in any Java platform to transform PreAward eCatalogues from Open Document Sheet formats to PEPPOL Conformant XML documents and vice versa

## Slide 22: Visualization Component
Page 22
  Decentral
  Reference Implementation visualisations are provided using via XSLT transformations which convert an original UBL document into HTML to be displayed in browsers or any other software with HTML rendering capabilities and are used to display PEPPOL documents in a clear, humanly readable format.

## Slide 23: Workflow Integration Component
Page 23
  Decentral
  PEPPOL BISs use BII profiles as the basis for standardizing the choreography of collaborations between two or more participants on the PEPPOL network. The technical implementation of this collaboration in the Demonstrator Client is using the OASIS Business Process Execution Language (BPEL) standard to describe the BIS on a technical level.

## Slide 24: Transport Infrastructure Component
Page 24
  Decentral
  A PEPPOL access point, which is responsible for the routing and the secure transport of the documents, uses either START (Secure Trusted Asynchronous Reliable Transport) or LIME (Lightweight Message Exchange Profile) transmission protocols.

## Slide 25
eProcurement without borders in Europe
www.peppol.eu